## Slide 1: Mobile Computing
Wireless Communication Systems

## Slide 2: DECT
Digital Enhanced Cordless Telecommunications
Also called
  Digital European cordless telephone and
  Digital European cordless telecommunications.
Replaces older analog cordless phone systems such as CT1 and CT1+.
Mainly used in offices, on campus, at trade shows, or in the home.
  Bridge the last few hundred meters between a new network operator and customers.

## Slide 3: Features and Characteristics
Local mobility in an in-building Private Branch Exchange (PBE)
Configured around an open standard.
  Allows to interconnect wide area fixed or mobile networks.
Range of DECT is limited to about 300 m from the base station.
  Can offer its service to some 10,000 people within one km2.
Provides low power radio access
  Each station has an average transmission power of only 10 mW with a maximum of 250 mW.
The digital modulation scheme is GMSK

## Slide 4: DECT Architecture
Based on OSI principles
A control plane (C-Plane) and user plane (U-Plane) use the services by lower layers.
Able to page upto 6000 subscribers
  No need of cell registration
Designed for radio local loop/ metropolitan are access.
Uses dynamic channel allocation.
Can also handle handover,
  But it was not designed to work at a higher speed.

## Slide 5: Contnd..
Physical Layer
  Uses FDMA/TDMA/TDD radio transmission method.
  Offering 120 full duplex channels.
  Within a slot one out of 10 carrier frequencies is used dynamically.
    Each frame (10ms duration) being divided into 24 slots using TDMA
      12 slots are used as uplink, 12 slots as downlink

## Slide 7: Contnd..
Medium Access Control (MAC) Layer
  Consists of paging channel and a control channel
    Transfers signaling information to the C-Plane.
  U-Plane is served with channels for the transfer of user information.
    The normal bit rate is 32kbps
  Supports hand off and a broadcast beacon service
    Enables all idle portable units to find the best fixed radio port to lock ratio.

## Slide 8: Contnd..
Data Link Control (DLC) Layer
  Provides reliable data links to the n/w layer
  Divides the logical and physical channels into time slots for each user.
  Provides formatting and error protection/correction for each time slot.

## Slide 9: Contnd..
Network Layer
  Main signaling layer.
  Based on ISDN and GSM protocols
  Provides
    Call control
    Circuit switched services selected from one of the DLC services
    Connection-oriented message services and mobility management

## Slide 10: Functional Concepts

## Slide 11: Contnd..
Portable Handset (PH)
  Mobile handset or terminal, cordless terminal adapters (CTAs)- fax or video communications.
Radio Fixed Part (RFP)
  Supports the physical layer of the DECT common air interface.
  Covers one cell in the microcellular system.
  Radio transmission between RFP and PH
    Multi Carrier TDMA
    Dulplex operation- using TDD

## Slide 12: Contnd..
Cordless Controller (CC or Cluster Controller)
  Central Control Unit
  Handles the MAC, DLC and network layers for one or a cluster of RFPs
  Speech coding is done in the CC using 32kbps ADPCM.
Network-Specific Interface Unit
  Supports the call completion facility in a multi-handset environment.
Supplementary Services
  Provides centralized authentication and billing
  Provides mobility management in PABX n/w.

## Slide 13: DECT Radio Link
DECT band-1880Mhz to 1900MHz
10 channels from 1881.792 to 1897.344
  With 1728kHz spacing
Base station supports FHMA on top of the TDMA/TDD structure.
Each slot may be assigned to a different channel
  Exploit the advantage of FH
  Avoid interference

## Slide 14: Contnd..
Channel Types
  User data: B-field
    320 bits+4bits parity
    32kbps per user
  Control data: A-field
    64 bits
    Assigned to one of the 4 logical channels.
    48 bits+16bits CRC
    6.4 kbps per user
    Relies on error detection and retransmission

## Slide 15: Contnd..
Speech Coding
  Speech is digitized into PCMusing 8kHz rate
  Speech samples are ADPCM encoded at 32kbps.
Channel Coding
  No channel coding and interleaving
    Frequency hopping
    End-to-end delay is tolerable
Modulation
  Tightly filtered GMSK
Antenna Diversity
  Implemented using 2 antennas.
  Best signal for each slot is selected
    Power or quality measured
  Fading and interference minimized.
Notes: ADPSM-Adaptive Digital Pulse Code Modulation

## Slide 17: Personal Access Communication Systems (PACS)
3rd Gen personal Communication System
Provides coverage within 500 meter range.
Objective is to integrate all forms of wireless local loop communications into one system with full telephone features.
A slightly altered proposed features
  10 TDMA/FDM time slots/2ms frame
  500 kbps channel data rate
  350kHz BW using QPSK->π/4 QPSK

## Slide 18: System Architecture
Operates in licensed or unlicensed PCS band.
May be connected to a PBX or Centrex
Served by a Central Office in residential applications.
Main Components
  Subscriber Unit (SU)
  Radio Ports (RPs)
  Radio Port Control Unit (RPCU)
  Access Manager(AM)

## Slide 19: Contnd..

## Slide 20: Contnd..
Interfaces
  A:
    The air interface, connection b/w SU&RP
  P:
    Provides the protocols required to connect the SUs through the RPs to the RPCU
    Connects the RPCU with its RPs by using an Embedded Operations Channel (EOC)
Standards contains a fixed distribution n/w and n/w intelligence.
  Only the last 500m of the distribution n/w is designed to be wireless.

## Slide 21: Frame Structure

## Slide 22: PACS Radio Interface
Designed for operation in the US PCS band
RF channels are Frequency or Time Division Multiplexed.
BW is 300kHz
TDMA with FDD
  8 slots in a 2.0ms frame
  Forward Link- 1850MHz to 1910MHz
  Reverse Link- 1930MHz to 1990 MHz
The reverse link time slot is offset from its paired forward link time slot by exactly one time slot and 62.5 µs
Unlicensed US PCS band b/w 1920 and 1930 MHz using TDD.

## Slide 23
Modulation
  π/4 QPSK modulation
  RF signal shaped using a raised cosine rolloff shaping filter
    99% of the transmitted signal power is contained within a channel BW of 288kHz
Speech Coding
  32kbps ADPCM
    Provides lox complexity, minimum Cost, and radio link privacy

## Slide 24: PACS Channels
  Provides system broadcasting channels (SBC)
    Used primarily on the forward link to broadcast paging message.
    32 kbps SBC provides altering and system information for upto 80000 users.
  Synchronization Channel (SYN) & slow Channel (SC)
    Used on forward link to synchronize each subscriber unit.
  Fast Channel
    User information transmission in both links

## Slide 25
Multiple Access
  Many portable handsets and data terminals may be served from one fixed Radio equipment.
  Radio links may be shared among customers on the basis of individual user activity.
    Provide wide range of user transmission rates with in a common architecture.
Power Control
  Uses adaptive power control to minimize battery drain
    To reduce co-channel interference on the reverse path

## Slide 26: System architecture (Optional)